## Slide 1: Lab. 04
Logic Design Lab.
Fall 2019
Prof. Sungjoo Yoo
(yeonbin@snu.ac.kr)
TA. Hyunsu Kim
(gustnxodjs@gmail.com)
TA. Hyunyoung Jung
(gusdud1500@gmail.com)

## Slide 2: Contents
Verilog
Lab
  Implement a Decoder in Verilog
  Implement a 3-to-8 Decoder using a 2-to-4 Decoder
Homework

## Slide 3: Verilog

## Slide 4: Overview
Hardware description languages (HDLs)
Types of programming
  Gate-level design
  Behavioral design / Register-transfer level design
Verilog Basics
  Verilog Notations
  Verilog Operators
  Verilog Keywords & Constructs

## Slide 5: Overview
Hardware description languages (HDLs)
Types of programming
  Gate-level design
  Behavioral design / Register-transfer level design
Verilog Basics
  Verilog Notations
  Verilog Operators
  Verilog Keywords & Constructs

## Slide 6: Hardware description languages (HDLs)
Different kinds of HDLs
  Abel (circa 1983) - developed by Data-I/O
  ISP (circa 1977) - research project at CMU
  Verilog (circa 1985) - developed by Gateway (absorbed by Cadence)
  VHDL (circa 1987) - DoD sponsored standard
Advantages of HDLs
  IEEE standard
  Common
  Flexible – Delay modeling, Matrices …
  Describe hardware at varying levels of abstraction
  ( = Describe hardware to other people briefly )

## Slide 7: Overview
Hardware description languages (HDLs)
Types of programming
  Gate-level design
  Behavioral design / Register-transfer level design
Verilog Basics
  Verilog Notations
  Verilog Operators
  Verilog Keywords & Constructs

## Slide 8: Types of programming
Describe hardware at varying levels of abstraction
Gate-level design
  Textual replacement for schematic
  Hierarchical composition of logic gates
Register-transfer level design
  Specify dataflow between hardware registers
(Synthesizable) Behavioral design
  Describe what module does, not how
  Synthesis generates circuit for module

## Slide 9: Overview
Hardware description languages (HDLs)
Types of programming
  Gate-level design
  Behavioral design / Register-transfer level design
Verilog Basics
  Verilog Notations
  Verilog Operators
  Verilog Keywords & Constructs

## Slide 10: Verilog Notations
Verilog is:
  Case sensitive(event-driven)
  Based on the programming language C
Comments
  Single Line
    // [end of line]
  Multiple Line
    /*
    …………
    …………
    */
List element separator: ,
Statement terminator: ;

## Slide 11: Verilog Notations
Binary Values for Constants and Variables
  0
  1
  X,x - Unknown
  Z,z – High impedance state (open circuit)
Constants
  n’b[integer]: 1’b1 = 1, 8’b1 = 000000001, 4’b0101 = 0101, 8’bxxxx = 0000xxxx
  n’h[integer]: 8’hA9 = 10101001, 16’hf1= 0000000011110001
Identifier Examples
  Scalar: A,C,RUN,stop,m,n
  Vector: sel[0:2], f[0:5], ACC[31:0], SUM[15:0],
  sum[15:0]

## Slide 12: Overview
Hardware description languages (HDLs)
Types of programming
  Gate-level design
  Behavioral design / Register-transfer level design
Verilog Basics
  Verilog Notations
  Verilog Operators
  Verilog Keywords & Constructs

## Slide 13: Verilog Operators
Bitwise Operators
    ~ NOT
    & AND
    | OR
    ^ XOR
    ^~ or ~^ XNOR
  Example:
  input[3:0] A, B;
  output[3:0] Z ;
  assign Z = A | ~B; // Z = A + B’

## Slide 14: Verilog Operators
Logical & Relational Operators
!, &&, | |, = =, !=, >=, <=, >, <, etc.
Arithmetic Operators
  +, -, etc.
Concatenation & Replication Operators
  {identifier_1, identifier_2, …}
  {n{identifier}}
  Examples: {REG_IN[6:0],Serial_in}, {8 {1’b0}}

## Slide 15: Overview
Hardware description languages (HDLs)
Types of programming
  Gate-level design
  Behavioral design / Register-transfer level design
Verilog Basics
  Verilog Notations
  Verilog Operators
  Verilog Keywords & Constructs

## Slide 16
module – fundamental building block for Verilog designs
  Used to construct design hierarchy
  Cannot be nested
endmodule – ends a module – not a statement
=> no “;”
Module Declaration
  module module_name (module_port, module_port, …);
  Example: module full_adder (A, B, c_in,
  c_out, S);
  …
  endmodule
Verilog Keywords & Constructs

## Slide 17
Input Declaration
  Scalar
    input list of input identifiers;
    Example: input A, B, c_in;
  Vector
    input[range] list of input identifiers;
    Example: input[15:0] A, B, data;
Output Declaration
  Scalar Example: output c_out, OV, MINUS;
  Vector Example: output[7:0] ACC, REG_IN, data_out;
Wire Declaration
  Scalar Example: wire t1, t2;
  Vector Example: wire[7:0] t1, t2;
Verilog Keywords & Constructs

## Slide 18: Verilog Keywords & Constructs
wire and reg
Values must be retained over time
  Register type: reg
  The reg in contrast to wire stores values between executions of the process
We can set values on reg, but cannot on wire

## Slide 19: Verilog Keywords & Constructs
Primitive Gates
  buf, not, and, or, nand, nor, xor, xnor
  Syntax:
  gate_operator instance_identifier (output, input_1, input_2, …)
  Example:
    or O1 (t1, A, B)
    O2 (t2, B, C, D);
    // t1=A+B, t2=B+C+D
    and A1 (OUT, t1, t2);
    // OUT = t1•t2 (OUT = (A+B)•(B+C+D))

## Slide 20: Verilog Keywords & Constructs
Process
  The body of a process consists of procedural statement to make desired outputs from inputs as like a common programming
  Processes are running in parallel
  initial – executes only once beginning at t = 0
  Only works on simulation – cannot be synthesized!
    Syntax: initial Statement; initial begin Statement; Statement; … end
  always – executes at t = 0 and repeatedly thereafter following repeat conditions.
    Syntax: always Repeat condition Statement; always Repeat condition begin Statement; Statement; … end

## Slide 21: Verilog Keywords & Constructs
  Timing Control Statement (for repeat conditions)
  The body of the process consists of procedural assignments
    Blocking assignments
      Example: C = A + B;
      Execute sequentially as in a programming language
    Non-blocking assignments
      Example: C <= A + B;
      Evaluate right-hand sides, but do not make any assignment until all right-hand sides evaluated. Execute concurrently unless delays are specified.
Type | Syntax | Description
Delay Control | #10 | Delay 10 unit time
Event Control | @(a) | Wait until signal ‘a’ is changed
 | @(posedge a) @(negedge a) | Wait until signal ‘a’ is changed to ‘1’ Wait until signal ‘a’ is changed to ‘0’
Level Control | wait (a==0) | Wait until signal ‘a’ is equal to ‘0’

## Slide 22: Verilog Keywords & Constructs
  Examples:
  Always @(*)
  begin
  B = A;
  C = B;
  end
  Suppose initially A = 0, B = 1, and C = 2
  After execution, B = 0 and C = 0
  Always @(*)
  begin
  B <= A;
  C <= B;
  end
  Suppose initially A = 0, B = 1, and C = 2
  After execution, B = 0 and C = 1

## Slide 23: Verilog Keywords & Constructs
  Conditional constructs
    The if-else
      If (condition)
      begin procedural statements end
      {else if (condition)
      begin procedural statements end}
      else
      begin procedural statements end
    The case
      case expression
      {case expression : statements}
      endcase;

## Slide 24: Lab

## Slide 25: Today
Design a 74x139(dual 2-to-4 decoder) in Verilog
  Practice all designing methods for half 74x139 each and simulate them
    Gate-level
    Behavioral / RTL
  Implement a 74x139 and simulate it
    Prepare simulations for all possible input combinations

## Slide 26: Designing 74x139(Dual 2-to-4 decoder)
G
A_L
B_L
A_i
B_i
U1
U2
U3
U4
U5
U6
U7
U8
U9
Schematic design of a 74x139

## Slide 27: Designing 74x139(Dual 2-to-4 decoder)
Gate level design (Half 74x139)
  Circuit function can be described with gate primitives

## Slide 28: Designing 74x139(Dual 2-to-4 decoder)
RTL design (Half 74x139)
    Circuit function can be described by assign(assign/always) statements and the conditional operator with binary combinations as in a truth table

## Slide 29: Designing 74x139(Dual 2-to-4 decoder)
Behavioral design (Half 74x139)
    Circuit function can be described by assign(assign/always) statements and the conditional operator with binary combinations as in a truth table

## Slide 30: Create a new Verilog project

## Slide 31: Set the project name, location, type

## Slide 32: Set the project name, location, type

## Slide 33: Create a new Verilog source

## Slide 34: Create a new Verilog source
or

## Slide 35: Write your own Verilog codes

## Slide 36: Compile and check errors

## Slide 37: Create a Verilog test bench

## Slide 38: Write a Verilog test bench codes

## Slide 39: Simulate it

## Slide 40: Simulation result

## Slide 41: Create a new Verilog source

## Slide 42: Re-write a Verilog test bench codes

## Slide 43: Designing 74x139(Dual 2-to-4 decoder)
Hierarchical Design (2  ½ 74x139)
    You make higher level module with the modules you already made
Y_L2

## Slide 44: Homework

## Slide 45: Homework
Implement 3-to-8 decoder and simulate it
  You have to re-use your 2-to-4 decoder implemented in lab
Implement 4-to-1 MUX and simulate it
  Implement in gate and rtl/behavior level
  Discuss two methods(Pros & Cons, etc.)
Implement 16-to-1 MUX and simulate it
  You have to re-use your 4-to-1 MUX implemented above
Given a four-input Boolean function
F(A,B,C,D) = Σ m(0,2,4,5,8,10,12,13,14,15),
implement the function using a 16-to-1 MUX
  You have to re-use YOUR 16-to-1 MUX implemented above

## Slide 46: Homework(Cont’d)
5. Design a 2x2-bit multiplier.
  Implement in Verilog and simulate it
  (TIP) This is a 2x2-bit multiplier that generates 4 bit output (whose MSB is
  P8 and LSB is P1). Note that A2 and B2 are MSBs.

## Slide 47: Report
Write a report
  # of pages doesn’t matter
  Include codes and simulation result
  The file size should not exceed 15MB
  Due : 7 Oct. (Before class begin at 7:00pm)

## Slide 48: Appendix

## Slide 49: An Example: Port Connection