## Slide 1: Lab. 05
Logic Design Lab.
Fall 2019
Prof. Sungjoo Yoo
(yeonbin@snu.ac.kr)
TA. Hyunsu Kim
(gustnxodjs@gmail.com)
TA. Hyunyoung Jung
(gusdud1500@gmail.com)

## Slide 2: Contents
BCD to 7-segment Decoder
FPGA
Introduction to SNU Logic Design Board
Lab
Homework

## Slide 3: BCD to 7-segment Decoder

## Slide 4: 7-segment Display
PIN
E
D
C
DP
G
F
A
B
VCC or GND
A form of electronic display device for displaying decimal numerals that is an alternative to the more complex dot-matrix displays.
Widely used in digital clocks, electronic meters, and other electronic devices for displaying numerical information.

## Slide 5: BCD to 7-segment Decoder
We need a decoder like above
So we will make it
?
A
B
C
D
E
F
G
7-segment
Outputs
i0
i1
i2
i3
BCD
Input Signal

## Slide 6: BCD to 7-segment Decoder (cont’d)
Step
Make a truth table with BCD and 7-segment outputs
  Which covers 0~9
Make Boolean expressions using K-map
Minimize them
Implement a decoder according to the expressions

## Slide 7: FPGA and SNU LD Board

## Slide 8: What is FPGA?
FPGAs(Field Programmable Gate Arrays) are semiconductor devices that can be programmed
  2-D array of logic blocks and flip-flops with electrically programmable interconnections
  Programmable Logic Device(PLD) with high density and capable of implementing different functions faster.
  Functionalities of an FPGA can be (re)programmed by downloading a configuration into the device
Users configure
intersection between logic blocks
and function of each block

## Slide 9: SNU Logic Design Board

## Slide 10: SNU Logic Design Board
FPGA(Spartan-3AN TQG144)

## Slide 11: SNU Logic Design Board
I/O Connectors

## Slide 12: SNU Logic Design Board
Connect to PC with Xilinx Platform Cable USB
  Connect each tag to the matching pin
  Connect the USB cable to PC

## Slide 13: Lab

## Slide 14: Today
Implement BCD to 7-segment Decoder on Xilinx ISE in 1) gate level description
2) RTL or behavioral description
and then simulate each of them.

## Slide 15: Homework
1.
Implement ‘Klingon number system’ decoder for 7-segment in
gate level description
RTL or behavioral description
And simulate each of them
Pic. Klingon number system

## Slide 16: Homework
16
2.
Implement 1-bit Arithmetic Logic Unit (ALU) in Verilog
  Follow the specification (a)
  Implement ALU module in Verilog and simulate it with Verilog test bench
  You should verify your implementation by testing all inputs in the truth table (b) with test bench
3 Control inputs
3 Data inputs
2 Data outputs
(a) specification
(b) truth table

## Slide 17: Report
Write a report
  # of pages doesn’t matter
  Include codes and simulation results
  The file size should be less than 15MB
  Due : 14 Oct. (Before class begin at 7:00pm)